## Slide 1: UFCFVK-15-2 Internet of Things
Bluetooth

## Slide 2: Bluetooth Low Energy (4.x and 5.0)
Hardware perspecive

## Slide 4: Short range wireless application areas
 | Voice | Data | Audio | Video | State
Bluetooth Asynchronous Connection Less / High Speed | x | Y | Y | x | x
Bluetooth Synchronous Connection Oriented /enhanced SCO | Y | x | x | x | x
Bluetooth low energy | x | x | x | x | Y
Wi-Fi | (VoIP) | Y | Y | Y | x
Wi-Fi Direct | Y | Y | Y | x | x
ZigBee | x | x | x | x | Y
ANT | x | x | x | x | Y
Low Power
State = low bandwidth, low latency data

## Slide 5
Zigbee devices can transmit data over long distances by passing data through a mesh network of intermediate devices to reach more distant ones. Zigbee is typically used in low data rate applications that require long battery life and secure networking.
Advanced and Adaptive Network Technology,” which is a low-energy wireless protocol meant to collect and transfer sensor data
Worldwide 2.4GHz ISM band operation
Ideal for sports and fitness devices
Very easy-to-use
Advanced networking capabilities

## Slide 6: What is Bluetooth LE
Bluetooth low energy is a NEW, open, short range radio technology
  Different to Bluetooth classic (BR/EDR)
  Basic Rate/Enhanced Data Rate (BR/EDR), is a low power radio that streams data over 79 channels in the 2.4GHz unlicensed industrial, scientific, and medical (ISM) frequency band
  Optimized for ultra low power
  Enable coin cell battery use cases
  < 20mA peak current
  < 5 uA average current

## Slide 7: Basic Concepts of Bluetooth LE
Everything is optimized for lowest power consumption
  Short packets reduce TX peak current
  Short packets reduce RX time
  Less RF channels to improve discovery and connection time
  Simple state machine
  Single protocol
  And so on.

## Slide 8: Bluetooth low energy factsheet 1
Range: | ~ 150 meters open field (1000 for BLE 5.x)
Output Power: | ~ 10 mW (10dBm)
Max Current: | ~ 15 mA
Latency: | 3 ms speed
Topology: | Star
Connections: | > 2 billion
Modulation: | GFSK @ 2.4 GHz
Robustness: | Adaptive Frequency Hopping, 24 bit CRC
Security: | 128bit AES CCM
Sleep current: | ~ 1μA
Modes: | Broadcast, Connection, Event Data Models, Reads, Writes

## Slide 9
Latency measures delay. Delay is simply the time taken for a data packet to reach its destination after being sent. We measure network latency as round trips, although it may sometimes be measured in one-way trips.

## Slide 10: Bluetooth low energy factsheet 3
Data Throughput
  For Bluetooth low energy, data throughput is not a meaningful parameter. It does not support streaming.
  It has a data rate of 1Mbps, but is not optimized for file transfer.
  It is designed for sending small chunks of data (exposing state)

## Slide 11: Designed for exposing state
It’s good at small, discrete data transfers.
Data can triggered by local events.
Data can be read at any time by a client.
Interface model is very simple (GATT)
A GATT service is a collection of characteristics.
For example, the heart rate service contains a heart rate measurement characteristic and a body location characteristic, among others. Multiple services can be grouped together to form a profile.
23.2˚C
Gate 10 BOARDING
12:23 pm
60.5 km/h
3.2 kWh
PLAY >>
Network Available

## Slide 12: Bluetooth Low Energy Architecture

## Slide 13
Physical Layer :
• The transmitter uses GFSK modulation and operates at unlicensed 2.4 GHz frequency band. • Using this PHY layer, BLE offers data rates of 1 Mbps (Bluetooth v4.2)/2 Mbps (Bluetooth v5.0). • It uses frequency hopping transceiver.
• Link Layer :
This layer sits above the Physical layer. It is responsible for advertising, scanning, and creating/maintaining connections.

## Slide 15
SMP :This security Manager layer provides methods for device pairing and key distributions. It offers services to other protocol stack layers in order to securely connect and exchange data between BLE devices. • GAP : This layer directly interfaces with application layer and/or profiles on it. It handles device discovery and connection related services for BLE device. It also takes care of initiation of security features. • GATT : This layer is service framework which specifies sub-procedures to use ATT. Data communications between two BLE devices are handled through these sub-procedures. The applications and/or profiles will use GATT directly. • ATT : This layer allows BLE device to expose certain pieces of data or attributes.

## Slide 16: Device Modes
Dual Mode
  Bluetooth BR/EDR and BLE
  Used anywhere that BR/EDR is used today
Single Mode
  Implements only Bluetooth LE
  Used in newer devices / applications

## Slide 17: Device Modes
Dual mode + single modes
BR/EDR stack
Dual-mode stack
Single-mode stack

## Slide 18
Serial Port Profile defines the protocols and procedures that shall be used by devices using Bluetooth for RS232 (or similar) serial cable emulation.
The Bluetooth protocol RFCOMM is a simple set of transport protocols, made on top of the L2CAP protocol, providing emulated RS-232 serial ports (up to sixty simultaneous connections to a Bluetooth device at a time)
L2CAP is used within the Bluetooth protocol stack. It passes packets to either the Host Controller Interface (HCI) or, on a hostless system, directly to the Link Manager/ACL link.
L2CAP's functions include: Multiplexing data between different higher layer protocols.
LMP establishes logical links between Bluetooth devices and maintains the links for enabling communications

## Slide 19
The Link layer is the second lowest protocol in the Bluetooth Low Energy protocol stack.
It’s responsible for managing the state of the LE radio, among other things.
To do this, the Link layer relies on a state machine.
So, what’s a state machine? In short, it’s a model that defines how a system should behave under certain conditions.

## Slide 20: Physical Layer
2.4 GHz ISM band
1Mbps GFSK
  Larger modulation index than Bluetooth BR (which means better range)
40 Channels on 2 MHz spacing

## Slide 21: Physical Channels
Two types of channels

## Slide 22: Physical Channels
Advertising channels avoid 802.11

## Slide 23: Link Layer
Link Layer state machine

## Slide 24: Advertising
Devices can advertise for a variety of reasons:
  To broadcast
  To transmit signed data to a previously bonded device
  To advertise their presence to a device wanting to connect
  To reconnect asynchronously due to a local event

## Slide 25: Data transactions
Once a connection is made:
  Master informs slave of hopping sequence and when to wake
  All subsequent transactions are performed in the 37 data channels
  Transactions can be encrypted
  Both devices can go into deep sleep between transactions

## Slide 26: Link Layer Connection
Very low latency connection
Central

## Slide 27
Thank you