## Slide 1: UFCFVK-15-2 Internet of Things
Network protocols

## Slide 2: TCP/IP

## Slide 3: TCP/IP Protocol Family
IP : Internet Protocol
  UDP : User Datagram Protocol
    RTP, traceroute
  TCP : Transmission Control Protocol
    HTTP, FTP, ssh

## Slide 4: What is an internet?
A set of interconnected networks
The Internet is the most famous example
Networks can be completely different
  Ethernet, ATM, modem, …
  (TCP/)IP is what links them

## Slide 5: What is an internet? (cont)
Routers (nodes) are devices on multiple networks that pass traffic between them
Individual networks pass traffic from one router or endpoint to another
TCP/IP hides the details as much as possible

## Slide 6: ISO/OSI Network Model
Seven network “layers”
  Layer 1 : Physical – cables
  Layer 2 : Data Link – Ethernet
  Layer 3 : Network – IP
  Layer 4 : Transport – TCP/UDP
  Layer 5 : Session
  Layer 6 : Presentation
  Layer 7 : Application
You don’t need to know the layers just the idea that it is layered

## Slide 7: OSI: Open Systems Interconnect OSI and Protocol Stack
OSI Model
TCP/IP Hierarchy
Protocols
7th
Application Layer
6th
Presentation Layer
5th
Session Layer
4th
Transport Layer
3rd
Network Layer
2nd
Link Layer
1st
Physical Layer
Application Layer
Transport Layer
Network Layer
Link Layer
Link Layer : includes device driver and network interface card
Network Layer : handles the movement of packets, i.e. Routing
Transport Layer : provides a reliable flow of data between two hosts
Application Layer : handles the details of the particular application

## Slide 8
Address Resolution Protocol (ARP)
It is a procedure for mapping a dynamic IP address to a permanent physical machine address in a local area network (LAN). The physical machine address is also known as a media access control (MAC) address.
The job of ARP is essentially to translate 32-bit addresses to 48-bit addresses and vice versa. This is necessary because IP addresses in IP version 4 (IPv4) are 32 bits, but MAC addresses are 48 bits.
ARP works between Layers 2 and 3 of the Open Systems Interconnection model (OSI model). The MAC address exists on Layer 2 of the OSI model, the data link layer. The IP address exists on Layer 3, the network layer.

## Slide 9
1110 0000
0001 0001
1000 0100
0000 0110
224
17
132
6
First half (3 bytes, 24 bytes) of multicast MAC will always be 01:00:5E
The second half of the MAC comes from the last 23 bits of the Multicast IP address
1110 0000
0001 0001
1000 0100
0000 0110
11
04
06
In hex
Final MAC for the multicast group would be
01:00:5E
:04:06:11

## Slide 10: RARP
  Client computer to request its IP address from a gateway server’s Address Resolution Protocol table or cache.
  The network administrator creates a table in gateway-router, which is used to map the MAC address to corresponding IP address.
  This protocol is used to communicate data between two points in a server.
  The client doesn’t necessarily need prior knowledge, the server identities capable of serving its request.
  Medium Access Control (MAC) addresses requires individual configuration on the servers done by an administrator.
  RARP limits to the serving of IP addresses only.

## Slide 12
Point - to - Point Protocol (PPP) is a communication protocol of the data link layer that is used to transmit multiprotocol data between two directly connected (point-to-point) computers.
Services Provided by PPP
Defining the frame format of the data to be transmitted.
Defining the procedure of establishing link between two points and exchange of data.
Method of encapsulation of network layer data in the frame.
Stating authentication rules of the communicating devices.
Providing address for network communication.
Providing connections over multiple links.

## Slide 13: Packet Encapsulation
The data is sent down the protocol stack
Each layer adds to the data by prepending headers
22Bytes
20Bytes
20Bytes
4Bytes
64 to 1500 Bytes

## Slide 14: IP
Responsible for end to end transmission
Sends data in individual packets
Maximum size of packet is determined by the networks
  Fragmented if too large
Unreliable
  Packets might be lost, corrupted, duplicated, delivered out of order

## Slide 15: IP addresses
4 bytes
  e.g. 163.1.125.98
  Each device normally gets one (or more)
  In theory there are about 4 billion available
But…

## Slide 16: Address range
Network Address | Usable Host Range | 
CLASS B
CLASS A
1.0.0.0 to 126.255.255.255
128.0.0.0 to 191.255.255.255
CLASS C
192.0.0.0 to 223.255.255.255
CLASS D
224.0.0.0 to 239.255.255.255
Reserved for Multicasting
CLASS E
240.0.0.0 to 254.255.255.255
Experimental
127.0.0.0 to 127.255.255.255 cannot be used and it is reserved for loopback testing

## Slide 17
Class A
Subnet-mask hides (or masks) the network part of a system's IP address and
A subnet mask leaves only the host part as the machine identifier.
255
MASK
0
0
0
.
.
.
1111 1111
0000 0000
0000 0000
0000 0000
.
.
.
1
2
3
4
5
6
7
8
20
Bit’s position
21
22
24
23
25
26
27
1
2
3
4
5
6
7
8
20
21
22
24
23
25
26
27
1st Octet all Network bits are absent
2nd & 3rd Octet all Network bits are absent
4th Octet all Network bits are present
An IPv4 address will have four sections of one to three numbers, separated by dots.

## Slide 18
The largest Class A networks use a subnet mask of 255.0.0.0, allowing for up to 16,777,216 IP addresses (256 x 256 x 256).

## Slide 19: CLASS - A
11 .
1111 1111 1000 0000 0000 0000 0000 0000
/9
12.
/9
11 .
45
Network bits
Network bit +Host bits
Host Bits
Host bits
1111 1111
1000 0000
0000 0000
0000 0000
255
128
0
0
2n
Where n is the number of network bits
21
=
2
Sub networks
2n
Where n is the number of host bits
=
27
128
Hosts per sub networks
_
2
2
_
126
=
_
Where the first 1 is the network address
2
Where the second 1 is the broadcast address
To find the number of subnets and hosts in each subnet we need to choose the octet which has the combination of 0’s & 1’s

## Slide 20
0
1
2
126
127
128.0.1
128.0.2
128.0.0
128.255.254
255.255
Network
Sub-Network 1
Sub-Network 2
11.0.0.0
11.127.255.255
11.0.0.1
11.128.0.0
11.255.255.255
Network address
Broadcast address
Network address
Broadcast address
Network Address | Usable Host Range | Broadcast Address:
11.0.0.0 | 11.0.0.1 to 11.126.255.254 | 11.127.255.255
11.128.0.0 | 11.128.0.1 to 11.255.255.254 | 11.255.255.255

## Slide 21: Routing
How does a device know where to send a packet?
  All devices need to know what IP addresses are on directly attached networks
  If the destination is on a local network, send it directly there

## Slide 22: Routing (cont)
If the destination address isn’t local
  Most non-router devices just send everything to a single local router
  Routers need to know which network corresponds to each possible IP address

## Slide 23: IP packets
Source and destination addresses
Protocol number
  1 = ICMP, 6 = TCP, 17 = UDP
Various options
  e.g. to control fragmentation
Time to live (TTL)
  Prevent routing loops

## Slide 24: IP Datagram
Vers
Len
TOS
Total Length
Identification
Flags
Fragment Offset
TTL
Protocol
Header Checksum
Source Internet Address
Destination Internet Address
Options...
Padding
Data...
0
4
8
16
19
24
31
Field Purpose
Vers IP version number
Len Length of IP header (4 octet units)
TOS Type of Service
T. Length Length of entire datagram (octets)
Ident. IP datagram ID (for frag/reassembly)
Flags Don’t/More fragments
Frag Off Fragment Offset
Field Purpose
TTL Time To Live - Max # of hops
Protocol Higher level protocol (1=ICMP,
6=TCP, 17=UDP)
Checksum Checksum for the IP header
Source IA Originator’s Internet Address
Dest. IA Final Destination Internet Address
Options Source route, time stamp, etc.
Data... Higher level protocol data
Notes: 16

## Slide 25: IP Routing
Routing Table
Destination IP address
IP address of a next-hop router
Flags
Network interface specification
Application
Transport
Network
Link
Application
Transport
Network
Link
Network
Link
Source
Destination
Router

## Slide 26: UDP
Thin layer on top of IP
Adds packet length + checksum
  Guard against corrupted packets
Also source and destination ports
  Ports are used to associate a packet with a specific application at each end
Still unreliable:
  Duplication, loss, out-of-orderness possible

## Slide 27: UDP datagram
Destination Port
Source Port
Application data
0
16
31
Checksum
Length
Field Purpose
Source Port 16-bit port number identifying originating application
Destination Port 16-bit port number identifying destination application
Length Length of UDP datagram (UDP header + data)
Checksum Checksum of IP pseudo header, UDP header, and data
Notes: 21

## Slide 28: Error Deduction through Check sum
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1
32 bit message

## Slide 29: Sender side
L
1 |  |  |  | 1 |  |  |  | 
 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0
 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1
 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 1
 |  |  |  |  |  |  |  | 1
 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0
 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1
sum
carry
Wrap sum
1’s Complement
Checksum

## Slide 30: Receiver side
L
1 |  |  |  | 1 |  | 1 | 1 | 
 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0
 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1
 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1
 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0
 |  |  |  |  |  |  |  | 1
 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
sum
carry
Wrap sum
1’s Complement
Checksum
All 0’s No error

## Slide 31: Typical applications of UDP
Where packet loss etc is better handled by the application than the network stack
Where the overhead of setting up a connection isn’t wanted
  VOIP
  NFS – Network File System
  Most games

## Slide 32: TCP
Reliable, full-duplex, connection-oriented, stream delivery
  Interface presented to the application doesn’t require data in individual packets
  Data is guaranteed to arrive, and in the correct order without duplications
    Or the connection will be dropped
  Imposes significant overheads

## Slide 33: Applications of TCP
Most things!
  HTTP, FTP (port number 21), SFTP/SSH (port number 22) …

## Slide 34: TCP implementation
Connections are established using a three-way handshake
Data is divided up into packets by the operating system
Packets are numbered, and received packets are acknowledged
Connections are explicitly closed
  (or may abnormally terminate)

## Slide 36: TCP Packets
Source + destination ports
Sequence number (used to order packets)
Acknowledgement number (used to verify packets are received)

## Slide 37: TCP Segment
Destination Port
Acknowledgment Number
Options...
Padding
Data...
0
4
10
16
19
24
31
Source Port
Window
Len
Sequence Number
Reserved
Flags
Urgent Pointer
Checksum
Field Purpose
Source Port Identifies originating application
Destination Port Identifies destination application
Sequence Number Sequence number of first octet in the segment
Acknowledgment # Sequence number of the next expected octet (if ACK flag set)
Len Length of TCP header in 4 octet units
Flags TCP flags: SYN, FIN, RST, PSH, ACK, URG
Window Number of octets from ACK that sender will accept
Checksum Checksum of IP pseudo-header + TCP header + data
Urgent Pointer Pointer to end of “urgent data”
Options Special TCP options such as MSS and Window Scale
You just need to know port numbers, seq and ack are added
Notes: 27

## Slide 38: TCP : Data transfer
Host
Client
Send Packet 1
Start Timer
Retransmit Packet1
Start Timer
Packet should arrive
ACK should be sent
ACK would normally
Arrive at this time
Receive Packet 1
Send ACK 1
Time Expires
Receive ACK 1
Cancel Timer
Packet Lost
Timer
Timer

## Slide 39: IPv6
128 bit addresses
  Make it feasible to be very wasteful with address allocations
Lots of other new features
  Built-in autoconfiguration, security options, …
Not really in production use yet