## Slide 1: UFCFVK-15-2 Internet of Things

## Slide 2: Introduction to Communication Systems and Networks

## Slide 3: Telecommunications
Tele (Far) + Communications
Early telecommunications
  smoke signals and drums
  visual telegraphy (or semaphore in 1792)
Telegraph and telephone
  Telegraph (1839)
  Telephone (1876)
Radio and television
Telephony
  Voice and Data

## Slide 4: Communications and Networks
Data Communications
  Transmission of signals
    Encoding, interfacing, signal integrity, multiplexing etc.
Networking
  Topology & architecture used to interconnect devices
Networks of communication systems

## Slide 5
Microcontroller
Networking
Wireless
Voice, Image, Data, Video
Integrated Systems!

## Slide 6: Communication Systems
Process describing transfer of information, data, instructions between one or more systems through some media
  Examples
    people, computers, cell phones, etc.
    Computer communication systems
Signals passing through the communication channel can be Digital, or analog
    Analog signals: continuous electrical waves
    Digital signals: individual electrical pulses (bits)
Receivers and transmitters: desktop computers, mainframe computers, etc.
TX
RX
RX
RX
Communication channel
Communication
media
Amp/Adaptor
An amplifier is an electronic device that increases the voltage, current, or power of a signal. Amplifiers are used in wireless communications and broadcasting, and in audio equipment of all kinds

## Slide 7: Communication Systems

## Slide 8: Communications Components
Basic components of a communication system
  Communication technologies
  Communication devices
  Communication channels
  Communication software

## Slide 9: A Communications Model

## Slide 10: Communications Tasks
Transmission system utilization | Addressing
Interfacing | Routing
Signal generation | Recovery
Synchronization | Message formatting
Exchange management | Security
Error detection and correction | Network management
Flow control | 

## Slide 11: Data Communications Model

## Slide 12: Communication Technology Applications
voice mail
Twitter
e-mail
instant messaging
chat rooms
newsgroups
telephony
videoconferencing
collaboration
groupware
global positioning system (GPS)

## Slide 13: Communication Technologies – Applications 1
Different technologies allowing us to communicate
  Examples: Voice mail, email, instant message, chat rooms, news groups, telephony, GPS, and more
Voice mail: Similar to answering machine but digitized
Email: electronic mail – sending text, files, images between different computer networks - must have email software
  More than 1.3 billion people send 244 billion messages monthly!

## Slide 14: Communication Technologies – Applications 2
Chat rooms: Allows communications in real time when connected to the Internet
Telephony: Talking to other people over the Internet (also called VoIP)
  Sends digitized audio signals over the Internet
  Requires Internet telephone software
Groupware: Software application allowing a group of people to communicate with each other (exchange data)
  Address book, appointment book, schedules, etc.
GPS: consists of receivers connected to satellite systems
  Determining the geographical location of the receiver
  Used for cars, advertising, hiking, tracking, etc.

## Slide 15: Communication Devices 1
Any type of hardware capable of transmitting data, instructions, and information between devices
  Functioning as receiver, transmitter, adaptor, converter
  Basic characteristics: How fast, how far, how much data!
Examples: Dial-up modems, ISDN, DSL modems, network interface cards
  Dial-up-modem uses standard phone lines
    Converts digital information into analog
    Consists of a modulator and a demodulator
    Can be external, internal, wireless
  ISDN and DSL Modem: Allows digital communication between networks and computers
    Requires a digital modem
    Digital is better than analog – why?

## Slide 16
ISDN : Integrated Services Digital Network.
It is used to bridge the Central Office's local loop and the premise connection (home). ISDN uses the existing wiring so that no new cabling is required. It is a digital service that restores the analog plain old telephone set.
An Integrated Digital Network (ISDN) is a network in which digital switching connections are used to transmit digital signals. Integrated Services refers to ISDNs ability to deliver two simultaneous connections, in any merging of data, voice, video and fax, over an individual line. Multiple devices can be connected to the line and sent as needed.
An ISDN is a network, in general evolving from telephony ISDN, which provides end-to-end digital connectivity to provide a broad range of services such as voice and non-voice services, to which customers have to create by a limited set of standard multipurpose user network interfaces.

## Slide 17
It offers symmetrical transfer rates− the transmit rate is the same as the receiving rate.
It has consistent transfer rates. If you have a 64 Kbps bearer channel, then it is the speed that you transfer at.

## Slide 18: Communication Devices 2
Examples: Dial-up modems, ISDN, DSL modems, network interface cards
  Network interface cards: Adaptor cards residing in the computer to transmit and receiver data over the network (NIC)
    Operate with different network technologies (e.g., Ethernet)
  Cable modem: a modem that transmits and receives data over the cable television (CATV) network
    Also called broadband modem (carrying multiple signals)
    The incoming signal is split
    Requires a cable modem

## Slide 19: Communication Software
Examples of applications (Layer 7) take advantage of the transport (Layer 4) services of TCP and UDP
  Hypertext Transfer Protocol (HTTP): A client/server application that uses TCP for transport to retrieve HTML pages.
  Domain Name Service (DNS): A name-to-address translation application that uses both TCP and UDP transport.
  Telnet: A virtual terminal application that uses TCP for transport.
  File Transport Protocol (FTP): A file transfer application that uses TCP for transport.

## Slide 20
Port numbers

## Slide 21: Communication Software
Examples of applications (Layer 7) take advantage of the transport (Layer 4) services of TCP and UDP
  Trivial File Transfer Protocol (TFTP): A file transfer application that uses UDP for transport.
  Network Time Protocol (NTP): An application that synchronizes time with a time source and uses UDP for transport.
  Border Gateway Protocol (BGP): An exterior gateway routing protocol that uses TCP for transport. BGP is used to exchange routing information for the Internet and is the protocol used between service providers.

## Slide 22: Communication Channels
A channel is a path between two communication devices
Channel capacity: How much data can be passed through the channel (bit/sec)
  Also called channel bandwidth
  The smaller the pipe the slower data transfer!
Consists of one or more transmission media
  Materials carrying the signal
  Two types:
    Physical: wire cable
    Wireless: Air
destination network server
T1 lines
T1 lines
T1 lines
T3 lines

## Slide 23: Physical Transmission Media
A tangible media
  Examples: Twisted-pair cable, coaxial cable, Fiber-optics, etc.
Twisted-pair cable:
  One or more twisted wires bundled together (why?)
  Made of copper
Coax-Cable:
  Consists of single copper wire surrounded by three layers of insulating and metal materials
  Typically used for cable TV

## Slide 24
Fiber-optics:
  Strands of glass or plastic used to transmit light
  Very high capacity, low noise, small size, less suitable to natural disturbances
plastic outer coating
woven or braided metal
insulating material
copper wire
twisted-pair cable
twisted-pair wire
protective coating
glass cladding
optical fiber core

## Slide 25: Wireless Transmission Media
Broadcast Radio
  Distribute signals through the air over long distance
  Uses an antenna
  Typically for stationary locations
  Can be short range
Cellular Radio
  A form of broadcast radio used for mobile communication
  High frequency radio waves to transmit voice or data
  Utilizes frequency-reuse

## Slide 26
Microwaves
  Radio waves providing high speed transmission
  They are point-to-point (can’t be obstructed)
  Used for satellite communication
Infrared (IR)
  Wireless transmission media that sends signals using infrared light- waves

## Slide 27: Networks
Collection of computers and devices connected together
Used to transfer information or files, share resources, etc.
What is the largest network?
Characterized based on their geographical coverage, speed, capacities
Networks are categorized based on the following characteristics:
  Network coverage: LAN, MAN, WAN
  Network topologies: how the computers are connected together
  Network technologies
  Network architecture

## Slide 28
A
B
C
Internet Server
Firewall
Intranet Server
Application Server
Other Server
X
Y
Intranet
Internet
Inter & Intra networks

## Slide 30: Types of Networks:
Local Area Network (LAN)
This is one of the categories of network, and one of the simplest. LAN networks connect computers together over relatively small distances, such as within a single building.

## Slide 31
Wide Area Network (WAN)
This is another categories of network, and slightly more complex in nature.
WAN networks connect computers together over large physical distances, remotely connecting them over one huge network and allowing them to communicate even when far apart.
The Internet is a WAN, and connects computers all around the world together.

## Slide 32: Wide Area Networks

## Slide 33
Metropolitan Area Network
This is a network which is larger than a LAN but smaller than a WAN, and incorporates elements of both. It typically spans a town or city and is owned by a single person or company, such as a local council or a large company.

## Slide 34: Metropolitan Area Network
Small Medium Enterprise
Small Office Home Office

## Slide 35
Topologies:
Devices must be connected using the following topologies:.
Mesh topology
Star topology
Ring topology
Bus topology

## Slide 37: Network Architecture
Refers to how the computer or devices are designed in a network
Basic types:
  Centralized – using mainframes
  Peer-2-Peer:
    Each computer (peer) has equal responsibilities, capacities, sharing hardware, data, with the other computers on the peer-to-peer network
    Good for small businesses and home networks
    Simple and inexpensive
  Client/Server:
    All clients must request service from the server
    The server is also called a host
    Different servers perform different tasks: File server, network server, etc.
client
client
client
server
laser printer

## Slide 38: P2P vs Client-Server
Peer-to-Peer Examples
Peers make a portion of their resources, such as processing power, disk storage or network bandwidth, directly available to other network participants, without the need for central coordination by servers or stable hosts

## Slide 39: (Data) Network Technologies
Vary depending on the type of devices we use for interconnecting computers and devices together
Ethernet:
  LAN technology allowing computers to access the network
  Susceptible to collision
  Can be based on BUS or STAR topologies
  Operates at 10Mbps or 100Mbps, (10/100)
  Fast Ethernet operates at 100 Mbps /
  Gigabit Ethernet (1998 IEEE 802.3z)
  10-Gigabit Ethernet (10GE or 10GbE or 10 GigE)
    10GBASE-R/LR/SR (long range short range, etc.)
Physical layer
  Gigabit Ethernet using optical fiber, twisted pair cable, or balanced copper cable

## Slide 40: (Data) Network Technologies
Token Ring
  LAN technology
  Only the computer with the token can transmit
  No collision
  Typically 72-260 devices can be connected together
TCP/IP and UDP
  Uses packet transmission
802.11
  Standard for wireless LAN
  Wi-Fi (wireless fidelity) is used to describe that the device is in 802.11 family or standards
  Typically used for long range (300-1000 feet)
  Variations include: .11 (1-2 Mbps); .11a (up to 54 Mbps); .11b (up to 11 Mbps); .11g (54 Mbps and higher

## Slide 41: (Data) Network Technologies
802.11n
  Current generation wireless LAN technology
  Improving network throughput (600 Mbps compared to 450 Mbps) – thus potentially supporting a user throughput of 110 Mbit/s
LORAWAN
  Low Power Wide Area Network
  Long disances
  Low Frequency (low-bandwidth)
  Ideal for Internet of Things
Zigbee
  High level communication protocols using small, low-power digital radios based on the IEEE 802.15.4
  Wireless mesh networking proprietary standard

## Slide 42: Network Technologies
Bluetooth 5
  Uses radio frequency (2.5ghz)
  Typically used for close distances (short range- 1000 feet or so)
  Transmits at 1Mbps
  Used for handheld computers to communicate with the desktop
IrDA
  Infrared (IR) light waves
  Transfers at a rate of 115 Kbps to 4 Mbps
  Requires light-of-sight transmission
RFID
  Radio frequency identification
  Uses tags which are places in items
  Example: merchandises, toll-tags, courtesy calls, sensors!

## Slide 43: Network Examples
IEEE 802.15.4
  Low-rate wireless personal area networks (LR-WPANs)
  Bases for e ZigBee, WirelessHART, and MiWi specification
  Also used for 6LoWPAN and standard Internet protocols to build a Wireless Embedded Internet (WEI)
Intranets
  Used for private networks
  May implement a firewall
    Hardware and software that restricts access to data and information on a network
Home networks
  Ethernet
  Phone line
  HomeRF (radio frequency- waves)
  Intelligent home network
Vehicle-to-Vehicle (car2Car) –
  A wireless LAN based communication system to guarantee European-wide inter-vehicle operability